## Slide 1
تحلیل داده ها
در مدیریت عملیات
دکتر عباس سقایی
Instagram.com/abbas.saghaei
abbas.saghaei@gmail .com
www.saghaei.ir

## Slide 2
کنترل فرایند آماری
هدف از کنترل فرآیند آماری کاهش میزان تغییرات و اجرای فرآیند در یک وضعیت تحت کنترل از لحاظ آماری می باشد.
وضعیتی که بتوان میان انحرافات با دلایل تصادفی و انحرافات با دلایل قطعی تمایز قائل شد.
بتوان پی برد که در کجا فرآیند به صورت کارآمد پیش می‌رود.
و اینکه چه زمانی محصول به اندازه کافی بازدهی دارد.
کنترل کیفیت آماری چند متغیره واقع گرایانه تر بوده اما پیچیده تر می باشد.
ارتقاء عملکرد
نظارت
بهبود
Notes: Statistical Control
The objective of SPC is to minimise variation and aim to run in a ‘state of statistical control’.
    Distinction between common cause (stochastic) variations and assignable cause
    Where process is operating efficiently
    When product is yielding sufficiently
MSPC more realistic representation but more complex
    Performance enhancement
    Monitoring
    Improvement

## Slide 3
Industry 4.0

## Slide 4
عبارت industry 4 بیانگر انقلاب صنعتی چهارم می باشد. دیگر عبارات مربوطه شامل اینترنت صنعتی یا کارخانه دیجیتال می شوند اما هیچکدام نمایی کامل را از این مفهوم ارائه نمی دهند. در دوره انقلاب سوم صنعتی تمرکز بر روی اتوماتیک سازی انفرادی ماشین ها و فرآیندها بود اما در انقلاب صنعتی چهارم تمرکز بر دیجیتال سازی فراگیر تمامی دارایی های فیزیکی و هماهنگ سازی آنها در قالب یک اکوسیستم دیجیتال میباشد. انقلاب صنعتی چهارم به واسطه ایجاد شبکه ای از تکنولوژی های نوین، دستاوردهایی را ازجمله تولید تحلیل و تبادل داده به همراه دارد.
Notes: What is it ?
the term ‘Industry 4.0’ stands for the fourth industrial revolution. Other related terms include the ‘Industrial Internet’ or the ‘Digital Factory’, although neither takes as complete a view. While Industry 3.0 focused on the automation of single machines and processes, Industry 4.0 focuses on the end-to-end digitization of all physical assets and integration into digital ecosystems with value chain partners. Generating, analysing and communicating data seamlessly underpins the gains promised by Industry 4.0, which networks a wide range of new technologies to create value.

## Slide 5
Industry 4.0– چهارمین انقلاب صنعتی

## Slide 6
چرا industry 4 ؟
صنعت چهارم یک تکنولوژی جدید و یا یک چارچوب در زمینه کسب و کار نیست بلکه رویکردی جدید به منظور دستیابی به نتایجی است که تا ده سال پیش قابل دسترسی نبودند.
انقلاب صنعتی چهارم حرکتی است به سمت دیجیتالیزه شدن.
صنعت چهارم از اینترنت اشیا و سیستم های فیزیکی مبتنی بر کامپیوتر مثل سنسورها که توانایی جمع آوری داده را داشته و می توانند به وسیله تولیدکنندگان استفاده شوند بهره می‌برد.
به کمک پیشرفتهای صورت گرفته در زمینه داده های کلان و تحلیل های قدرتمند سیستم ها می توانند با استفاده از داده های تولید شده بینش هایی به دست آورند که بتوان با کمک آن ها به سرعت به شرایط مختلف واکنش نشان داد.
زیربنای ارتباطی این تکنولوژی از امنیت کافی برخوردار بوده و می‌تواند به وسیله صنایع بزرگ استفاده شود.
Notes: Why Industry 4.0
Industry 4.0 is not a new technology, nor is it a business discipline, but in fact a new approach to achieve results that weren't possible 10 years ago thanks to advancements in technology.
The fourth industrial revolution, is the move towards digitisation.
Industry 4.0 will use the Internet of Things and cyber-physical systems such as sensors having the ability to collect data that can be used by manufacturers and producers.
the advancements in big data and powerful analytics means that systems can trawl through the huge sets of data and produce insights that can be acted upon quickly.
the communications infrastructure backing this up is secure enough to be used by heavy industries.

## Slide 7
صنعت چهارم تا چه میزان ارزشمند است ؟
بر اساس بررسی‌های صورت گرفته توسط KPMG تا سال ۲۰۲۰ بازار تکنولوژی های کاربردی در صنعت چهارم از ارزش بالغ بر ۴ تریلیون دلار برخوردار خواهند بود.
بر اساس گزارشی که اخیراً از جانب دولت انگلستان منتشر یافته استفاده از این تکنولوژی پیشرفته باعث سودآوری بخش تولیدات صنعتی به اندازه ۴۴۵ میلیون پوند خواهد شد و همچنین نزدیک به ۱۷۵ هزار شغل ایجاد خواهد کرد.
Notes: How much is Industry 4.0 worth?
Recent figures from KPMG has estimated that the component markets of Industry 4.0 are estimated to be worth more than US$4 trillion by 2020.
Businesses everywhere are thought to be able to benefit from embracing Industry 4.0, with a recent uk government report claiming that utilising this advanced technology could benefit the nation's manufacturing sector by around £445 billion and create around 175,000 jobs,

## Slide 8
چهارچوب عملکردی نسل چهارم انقلاب صنعتی و تکنولوژی هایی که در این نسل مشارکت دارند
Notes: Industry 4.0 framework and contributing digital technologies

## Slide 9: کارخانه هوشمند

## Slide 10: مورد کاوی تحلیل فرایند در یکی از بزرگترین صنایع فولادی کشور

## Slide 11: A Vocabulary of Confusion (Work in Progress)
Resource Management
Data Fusion
Sensor Fusion
Information
Fusion
Tracking
Data Mining
Correlation
Planning
Complex Event
Processing
Processing
Management
Sensor
Management
Control
Estimation
Event Stream
Processing
Adapted from: Steinberg, A., & Bowman, C., CRC Press, 2001

## Slide 12
Internet of things

## Slide 13
اینترنت اشیا چیست ؟
اینترنت اشیا شبکه ای از اشیاء فیزیکی همچون دستگاه‌ها، اتومبیلها، ساختمانها می باشد. هر کدام از این اشیا به اجزاهای الکترونیکی، نرم افزارها سنسور ها و قابلیت اتصال به شبکه مجهز شده اند که آنها را قادر می‌سازد داده ها را جمع‌آوری و مبادله کنند
Notes: What is it ?
The Internet of Things (IoT) is the network of physical objects—devices, vehicles, buildings and other items embedded with electronics, software, sensors, and network connectivity—that enables these objects to collect and exchange data.

## Slide 14
چرا از اینترنت اشیا استفاده کنیم ؟
استفاده از شبکه ای از اشیا متصل به هم که با یکدیگروهمچنین با کاربر به تبادل داده می‌ پردازند، می‌تواند میزان خدمت رسانی را ارتقا و همچنین ارزش بیشتری ایجاد کند
از مزایای استفاده از اینترنت اشیا می توان به موارد زیر اشاره نمود :
مدیریت هرچه بهتر دارایی ها
مصرف بهینه منابع
از میان برداشتن خطاهای انسانی
ایجاد بازدهی بالاتر و همچنین تسهیل امور برای کاربر
Notes: Why use it ?
Value proposition:
Greater value and service will be achieved by exchanging data with other connected devices or the user / operator
IoT enables:
Better management of assets
Efficient consumption of resources
Eliminate human error
Higher efficiency and convenience for the user

## Slide 15
بازار اینترنت اشیا
با بررسی های صورت گرفته توسط IDC پیش بینی شده است که هزینه های صورت گرفته بر روی اینترنت اشیا در سطح جهانی به ۷۷۲.۵ بیلیون دلار در سال ۲۰۱۸ خواهد رسید که افزایش ۱۵ درصدی را نسبت به هزینه های انجام شده ( ۶۷۴ بیلیون دلار) در زمینه اینترنت اشیا در سال ۲۰۱۷ نشان می‌دهد.
Notes: The IoT Market
According to IDC, worldwide spending on the IoT is forecast to reach $772.5B in 2018. That represents an increase of 15% over the $674B that was spent on IoT in 2017.

## Slide 16: اینترنت اشیا و زمینه های تحلیلی
Notes: IoT & Analytics

## Slide 17
چه بخشهایی از اینترنت اشیا استفاده می کنند ؟
بخش تولیدات
حمل و نقل
خرده فروشی
زمینه های علمی و تکنولوژی
فناوری اطلاعات و ارتباطات
تحصیلات
مراقبتهای درمانی و بهداشتی
انرژی
ساخت و ساز
Notes: What sectors use the IoT?
Manufacturing
Transportation
Retail
Science and Technology
IT and Communications
Education
Healthcare
Energy
Construction
Agriculture

## Slide 18
توسعه های صورت گرفته در زمینه کسب و کار به واسطه اینترنت اشیا
خرده فروشی
بررسی خودکار محصولات خریداری شده از جانب مشتریان
مدیریت انبار و موجودی
تولیدات صنعتی
بازدهی عملیات
تعمیرات و مدیریت دارایی
Notes: IoT business developments
Retail
Automated checkout
Inventory and warehouse management
Manufacturing
Operations efficiencies
Asset management and maintenance

## Slide 19
توسعه های صورت گرفته در زمینه کسب و کار به واسطه اینترنت اشیا
مصرف کنندگان
سرگرمی
سلامتی و تناسب اندام
بخش های دولتی
بازدهی و ذخیره انرژی
امنیت
Notes: IoT business developments
Consumers
Entertainment
Health and fitness
Offices and Government
Productivity and energy saving
Security and surveillance

## Slide 20
حمل و نقل
خودکار سازی و کنترل ترافیک
مدیریت ناوگان
مراقبت های بهداشتی درمانی
نظارت
اجرای خودکار فرآیندهای درمانی
توسعه های صورت گرفته در زمینه کسب و کار به واسطه اینترنت اشیا

## Slide 22
The Internet of Things & Manufacturing
IoT applications in mfg. and factory settings expected to generate $1.2 to $3.7 trillion of economic value annually by 2025.
IoT will revolutionize manufacturing processes.
IoT will revolutionize manufactured products and product systems.

## Slide 23
IoT and Manufacturing Processes
IoT will generate 4 primary forms of value in terms of manufacturing processes:
1.Supply Chain Management;
2.Operating Efficiency;
3.Predictive Maintenance;
4.Inventory Optimization.

## Slide 24
IoT and Supply Chain Management
IoT can help manufacturers better manage their supply chains.
BMW: Knows the real-time status of all machines producing all parts/components from all suppliers going into vehicles.
Toyota: Reduces recalls by knowing exactly what machine produced which components of which vehicles.
HP: Integrates network analysis and data visualization into its supply chain management and monitoring; has reduced the time for supply chain management projects by up to 50%.

## Slide 25
IoT and Manufacturing Operating Efficiency
IoT provides manufacturers a comprehensive view of what’s occurring at every point in the production process and helps make real-time adjustments.
Will increase manufacturing productivity by 10-25%.
Producing up to $1.8 trillion in global economic value by 2025.

## Slide 26
IoT and Manufacturing Operating Efficiency
Explosion of low-cost sensor technologies has made every manufacturing process and component a potential data source.
Ford: Placed sensors on virtually every piece of production equipment at its River Rouge facility.
GM: Uses sensors to monitor humidity conditions during vehicle painting; if unfavorable, the work piece is moved elsewhere in plant or ventilation systems adjusted.
Raytheon: Keeps track of how many times a screw has been turned in its factories.
Merck: Improves vaccines by conducting up to 15 billion calculations to determine what environmental and process factors influence quality of final product.

## Slide 27
IoT and Predictive Maintenance
Monitor the status of production equipment in real-time.
Intel: Uses predictive modeling to anticipate failures, prioritize inspections, and cut monitoring costs, save $3M.
Ford: Downstream machines can detect if work pieces they receive are off in a particular minute dimension, indicating possible problems in upstream machines.
GE “Brilliant Factories” initiative doubled production of defect-free dishwashers and washing machines.

## Slide 28
IoT and Predictive Maintenance
IoT expected to reduce factory equipment maintenance costs by up to 40%.
Expected to reduce equipment downtime by up to 50% and is expected to reduce capital equipment investment costs 5%.
Generating economic value of $630B annually by 2025.

## Slide 29
IoT and Inventory Optimization
IoT helps manufacturers better manage inventory.
Wurth USA: Developed an “iBins” system that uses intelligent camera technology to monitor the fill level of a supply box and wirelessly transmit the data to an inventory management system that automatically reorders supplies.
IoT can drive inventory optimization measures that can save 20 to 50% of factory inventory carrying costs.

## Slide 30
Other IoT Apps. In Mfg. Processes
Safety: IoT applied to devices and workers (e.g., badges) can alert or even halt equipment if in too close of proximity.
Leveraging data on factory equipment for usage-based design (improve equipment performance or reduce parts needed.)

## Slide 33
Asset management
(diagnostic and prognostic)

## Slide 34
در پاسخ به نياز روزافزون به انرژی الكتريكی در ايران و عدم توليد توربين و تجهيزات جانبی آن در كشور، شركت مهندسی و ساخت توربين مپنا (توگا) كه يكی از زيرمجموعه‌های اصلی گروه مپنا است در تابستان سال 1378 تاسيس و توليد توربين‌های بزرگ گازی در كارخانجات خود واقع در فرديس كرج (سی كيلومتری تهران) را از اواخر سال 1380 آغاز نمود. از آن زمان تاكنون و به منظور پوشش نياز رو به رشد داخلی و خارجی به اين محصولات، تأسيسات و ظرفيت كارخانه مرتباً افزايش يافته و به قريب 40 واحد در سال رسيده است.
در حال حاضر شركت توگا با ثبت توليد و تحويل بيش از 300 واحد توربين‌های گاز و بخار نيروگاهی به بازار ايران و منطقه خاورميانه در كارنامه خود، يك بازيگر بين‌المللی در صنعت توربين محسوب می‌گردد.
شرکت مهندسی و ساخت توربین مپنا (توگا)

## Slide 35
به منظور تولید قطعات مختلف توربین از ماشین آلات متعددی استفاده می گردد. به طور مثال جهت تولید پره های توربین از ماشین های پره زنی 5 محوره استفاده می گردد.
این ماشین از سه محور اصلی X , Y , Z و دو محور کمکی بهره می برد.
این ماشین دارای سنسور های مختلفی است که بواسطه آن ها می توان به داده های عملکرد ماشین دسترسی پیدا کرد و نسبت به سلامت ماشین اطمینان حاصل نمود. بخشی از این داده ها عبارتند از :
به ازای هرکدام از محور های X,Y,Z,A,B,U,S :
سرعت
دما
جریان
بارگذاری
گشتاور
موقعیت در جهت هر محور
پارامترهای الکتریکی :
متوسط جريانهاي سه فاز
جريان فاز 1
جريان فاز 2
جريان فاز 3
متوسط ولتاژ فاز به نول
ولتاژ فاز 1 نسبت به نول
ولتاژ فاز 2 نسبت به نول
ولتاژ فاز 3 نسبت به نول
متوسط ولتاژ خط به خط
ولتاژ فاز 1 نسبت به نول
ولتاژ فاز 2 نسبت به نول
ولتاژ فاز 3 نسبت به نول
cos phi موثر سه فاز
cos phi فاز1
cos phi فاز2
cos phi فاز3
ضريب توان موثر بر سه فاز توان اكتيو تقسيم بر توان ظاهري
ضريب توان فاز 1
ضريب توان فاز 2
ضريب توان فاز 3
مجموع توان هاي حقيقي سه فاز
توان حقيقي فاز 1
توان حقيقي فاز 2
توان حقيقي فاز 3
مجموع توان هاي مجازي سه فاز
توان مجازي فاز 1
توان مجازي فاز 2
توان مجازي فاز 3
مجموع توان هاي ظاهري سه فاز
توان ظاهري فاز 1
توان ظاهري فاز 2
توان ظاهري فاز 3
مجموع اعوجاج هارمونيكي ولتاژ فاز 1
مجموع اعوجاج هارمونيكي ولتاژ فاز 2
مجموع اعوجاج هارمونيكي ولتاژ فاز 3
مجموع اعوجاج هارمونيكي جريان فاز 1
مجموع اعوجاج هارمونيكي جريان فاز 2
مجموع اعوجاج هارمونيكي جريان فاز 3

## Slide 36
Prognostics and health management (PHM) is a new engineering approach that Enables :
real-time health assessment of a system under its actual operating conditions
prediction of system future state based on up-to-date information by incorporating various disciplines including sensing technologies, failure physics,machine learning, modern statistics, and reliability engineering
It enables engineers to turn data and health state into information that will improve our knowledge on the system and provides a strategy to maintain the system in its originally intended function.
Introduction

## Slide 37
Main steps of the PHM
The main steps of PHM include :
data acquisition
diagnostics
Prognostics
health management

## Slide 38
data acquisition
The first step is data acquisition, which is to collect measurement data from the sensors and process them to extract useful features for diagnosis.
diagnostics
The second step is the diagnostics, in which the fault is detected for any anomaly, isolated to determine which component is failing and to identify how severe it is with respect to the failure threshold.
Prognostics
Third step is the prognostics that predicts how long it will take until failure under the current operating condition.
health management
The last step is the health management to manage in optimal manner the maintenance scheduling and logistics support

## Slide 39
OSA/CBM
Among the standards proposed for the PHM process the Open System Architecture for Condition Based Maintenance (OSA/CBM) is the most popular, which consists of six phases or layers:
data acquisition : which is concerned with the activity of measuring data using a variety of sensors
data manipulation : which performs processing of raw data which then feeds into the condition monitoring layer.
condition monitoring : this layer calculates condition indicators and provides alarm capabilities for anomaly.
health assessment : uses the condition indicators to determine health status describing how bad it is in quantitative manner
Prognostics : In this layer, an estimate of future progress is made including the remaining useful life .
Data acquisition : Decision-making layer is to produce suitable measures for replacement, and maintenance activities based on the data from the previous layers.

## Slide 40
مروری بر الگوریتم های مورد استفاده در زمینه prognostics
In general, based on the usage of information, prognostics methods can be categorized into two approaches :
physics-based
data-driven approaches

## Slide 41
physics-based Approaches :
Physics-based approaches assume that a physical model describing the behavior of degradation is available and combine the physical model with measured data and usage conditions to identify model parameters and to predict the future behavior.
Since this approach needs to capture physical basis of failure in model that relates the forces that cause damage to their effect, it requires a detailed understanding of the problem.

## Slide 42
The most important advantage of physics-based method is that the results tend to be intuitive because they are based on modeled phenomenon. Also, once a model is developed, it can be reused for different systems or different designs by tuning model parameters. If incorporated early enough in design process, it can drive sensor requirements; that is adding or removing sensors. The method is generally considered as computationally efficient than the data-driven method.
However, the advantages of physics-based approaches can also work against them. For example, model development requires a thorough understanding of the system. If any important physical phenomenon is missed, then it can lead to failure of predicting degradation behavior. Also, high-fidelity models, especially for numerical models, can be computationally intensive.
physics-based Approaches :

## Slide 43
دامنه کاربرد اگوریتم های مبتنی بر فیزیک سیستم و الگوریتم های مبتنی بر داده
Notes: Application domains of physics-based and data-driven prognostics algorithms :

## Slide 44
Industrial Applications and case studies
Manufacturing applications
Heavy vehicle and mining application
Power generation application
Aerospace and defense applications
Automotive and electric vehicle application
Railway applications

## Slide 45
Instagram.com/abbas.saghaei
abbas.saghaei@gmail .com
www.saghaei.ir